## Slide 1
SmartCORE HEMS Box
Home Energy Management System — Research Development
Munster Technological University | Interreg NWE SmartCORE
Notes: Good morning / good afternoon everyone, and thank you for the opportunity to present today.
My name is [your name], I'm a researcher at Munster Technological University, and today I want to walk you through the Home Energy Management System — or HEMS box — that we've been developing here at MTU as part of the SmartCORE NWE project.
This is a ten-minute overview, so I'll move at a reasonable pace, but please do hold any questions until the end — I'll leave time for discussion.

## Slide 2
Notes: What I want to show you today is a working prototype of a piece of hardware and software that sits inside a home, connects to the smart meter, monitors energy consumption in real time, and makes that data available for research and for the householder themselves.
Let's get started.

## Slide 3
SmartCORE NWE — Project Context
Interreg North-West Europe | MTU's Role
MTU SmartCORE HEMS
Interreg NWE SmartCORE
• Interreg NWE transnational research project
• Partners across Ireland, Luxemburg, Belgium, France, Netherlands
• Focus: Community-scale smart energy management
• Objective: Reduce household energy costs & carbon footprint
• MTU leads the Ireland pilot workstream
• Responsible for: HEMS hardware + software stack development
• Target: Deploy HEMS units in Irish pilot homes
MTU Research Role
Design & build open-source HEMS gateway
Containerised, remotely manageable
Bridges Zigbee sensors → cloud analytics
Feeds SmartCORE data platform
Key Metrics (Target)
≥ 20 pilot homes in Ireland
Real-time energy monitoring
15-min resolution data to EU platform
OTA updates — no on-site visits
Notes: Just to set the scene briefly for anyone who may be new to this specific workstream.
SmartCORE NWE is an Interreg North-West Europe project involving research partners from Ireland, the UK, Belgium, France, and the Netherlands. The overarching goal is to demonstrate community-scale smart energy management — helping households and communities reduce their energy costs and their carbon footprint.
Within that wider project, MTU leads the Ireland pilot workstream. Our specific job is to design and build the HEMS hardware and software stack — the physical box that goes into a home and does the energy monitoring.
We then target deploying these units into pilot homes across the Munster region. The numbers we're working towards are at least twenty homes, providing fifteen-minute resolution energy data that feeds into the SmartCORE European data platform.
One of the things I'll emphasise throughout this presentation is that everything we're building is open-source, remotely manageable, and designed so that any partner organisation could in principle pick up the same design and deploy it in their own country without starting from scratch.

## Slide 4
The Challenge
Why do we need a bespoke HEMS gateway?
MTU SmartCORE HEMS
Interreg NWE SmartCORE
Fragmented Sensor Ecosystem
Zigbee, Z-Wave, BLE — no common protocol
Utility meters rarely IoT-ready
Off-the-shelf hubs lack research-grade data access
Data Sovereignty & Privacy
Cloud-dependent products = no local control
GDPR concerns with home energy data
Partners need raw data, not vendor-filtered APIs
Remote Manageability at Scale
30+ homes across Ireland — no on-site engineers
Firmware updates must be zero-touch
Self-healing critical — no single point of failure
Open & Extensible Research Platform
Off-the-shelf systems are black boxes
We need to add sensors, change algorithms, export data
Must integrate with SmartCORE EU data platform
Notes: So why are we building something ourselves rather than buying an off-the-shelf product? That's a fair question and I want to address it directly.
There are four core problems we identified.
First: the sensor ecosystem is fragmented. Smart home devices use different wireless protocols — Zigbee, Z-Wave, Bluetooth — and most commercial hubs don't give you raw data access. They give you a mobile app and a cloud subscription, and that's it.
Second: data sovereignty. For a research project, we need the raw energy data. We can't rely on a vendor's API that might change, or have data filtered or aggregated before we see it. And from a GDPR perspective, having home energy data flowing through a third-party cloud server in the US raises real compliance questions.
Third: remote manageability. Once we deploy twenty or thirty boxes across homes in Munster, we cannot send an engineer to each house every time there's a software update or a bug fix. The system has to update itself, heal itself, and keep running without any on-site intervention.
And fourth: we need an open, extensible research platform. Off-the-shelf products are black boxes. We need to be able to add new sensors, change data processing pipelines, export data in different formats, and integrate with the SmartCORE European platform — none of which is possible with consumer products.
Those four constraints are what drove us to build our own stack.

## Slide 5
The HEMS Box — What Is It?
An open, containerised edge gateway for residential energy monitoring
MTU SmartCORE HEMS
Interreg NWE SmartCORE
Hardware
Raspberry Pi 5 (arm64 / aarch64)
  – 4 GB RAM, Quad-core Cortex-A76
  – Runs BalenaOS (Yocto Linux)
Sonoff ZBDongle-E (USB)
  – EZSP Zigbee coordinator
  – IEEE 802.15.4 @ 2.4 GHz
Frient SMSZB-120
  – Smart meter interface sensor
  – Blink counter → power & energy
[ Photo placeholder: Pi 5 + USB dongle ]
Software Stack
BalenaOS — container OS + OTA
Docker Compose — 8 services
Home Assistant — data hub & UI
InfluxDB 2 — time-series database
Nginx — reverse proxy & auth
Mosquitto — MQTT broker
hass-configurator — config UI
system-manager — watchdog
led-status — GPIO health LEDs
Bridge network 172.18.4.0/24
Isolated, static IPs per service
Design Principles
Open-source throughout
No cloud dependency
(works fully offline)
Self-healing & self-updating
via BalenaOS Supervisor
Extensible — add sensors,
services, or integrations
without hardware changes
Research-grade data access
— full InfluxDB query API
Notes: So what exactly is the HEMS box? Let me describe it in concrete terms.
On the hardware side, it's built around a Raspberry Pi 5. That's a small, low-power single-board computer — roughly the size of a credit card, runs on about five watts, and costs around eighty euros. It runs a specialised operating system called BalenaOS, which is purpose-built for running containerised applications on edge devices.
Plugged into the Pi via USB is a Sonoff ZBDongle-E — this is a Zigbee coordinator stick. Zigbee is the wireless protocol used by many smart home sensors, and this dongle acts as the radio gateway that lets the Pi talk to those sensors.
The sensor we're currently working with is the Frient SMSZB-120, which is a smart meter interface device. It clips onto the optical port of an Irish smart meter, counts the infrared blink pulses the meter emits, and converts those into real-time power readings in watts and cumulative energy readings in kilowatt-hours. It communicates back to the Pi over Zigbee.
On the software side, everything runs as Docker containers — eight separate services, all managed together using Docker Compose. I'll walk through what each of those services does in a moment.
The key design principles are: fully open-source throughout, no cloud dependency — the system works completely offline if needed — self-healing and self-updating via the BalenaOS infrastructure, extensible without hardware changes, and providing research-grade data access.
Think of it as a small, silent, self-managing computer that lives in a kitchen cupboard and watches the electricity meter.

## Slide 6
System Architecture
8 containerised services on a private Docker bridge network
MTU SmartCORE HEMS
Interreg NWE SmartCORE
Raspberry Pi 5 (BalenaOS Host)
Docker Bridge 172.18.4.0/24
Home Assistant
172.18.4.2 :8123
InfluxDB 2
172.18.4.3 :8086
Nginx Proxy
172.18.4.4 :80
Mosquitto MQTT
172.18.4.7 :1883
hass- configurator
172.18.4.6 :3218
led-status
172.18.4.9 GPIO 17/27/22
system- manager
host network Supervisor API
wifi- connect
host network Captive portal
BalenaOS Supervisor
Balena Cloud (OTA updates)
Sonoff ZBDongle-E (USB / EZSP Zigbee coordinator)
Frient SMSZB-120 (Zigbee sensor)
← Zigbee 802.15.4 →
Notes: Now let me show you the architecture — how all the pieces fit together.
Everything you see here runs on a single Raspberry Pi 5. The outer box represents the Pi itself, running BalenaOS. Inside that, we have a Docker bridge network — a private internal network with the IP range 172.18.4.0/24. Each container gets its own fixed IP address on that network, which makes the system predictable and easy to debug.
Starting from the bottom: the Sonoff ZBDongle-E USB stick is passed directly into the Home Assistant container. Next to it is the Frient sensor, communicating over Zigbee 802.15.4 radio.
In the top row, you have our four core services. Home Assistant at 172.18.4.2 is the central hub — it manages the Zigbee network, processes sensor data, and provides the user dashboard. InfluxDB at 172.18.4.3 is our time-series database where all historical energy data is stored. The Nginx reverse proxy at 172.18.4.4 sits in front of everything and provides a single secure entry point on port 80. And Mosquitto at 172.18.4.7 is our MQTT message broker — more on that in a moment.
In the second row: hass-configurator provides a browser-based editor for the Home Assistant configuration files. The led-status container drives three physical LEDs on the Pi's GPIO pins to give a visual health indication. The system-manager is a watchdog process that keeps everything running. And wifi-connect handles the initial WiFi setup when the box is first installed in a home.
On the right, you can see the BalenaOS Supervisor — the daemon that communicates with Balena Cloud and handles over-the-air updates.
The whole thing is entirely self-contained. Unplug it, move it to a different home, power it on, and it just works.

## Slide 7
Energy Data Flow
From physical smart meter pulse to database — end-to-end
MTU SmartCORE HEMS
Interreg NWE SmartCORE
Smart Meter
IR pulse output (blink counter)
→
Frient SMSZB-120
Counts pulses → kWh / W
→
Sonoff ZBDongle-E
USB Zigbee coordinator (EZSP)
→
ZHA (in HA)
Zigbee Home Automation integration
→
HA State Machine
Entity states updated every 60 s
→
InfluxDB Integration
HTTP POST Line Protocol → InfluxDB
→
InfluxDB 2
Time-series DB bucket: home_assistant
Zigbee 802.15.4
EZSP/USB serial
HA internal bus
HTTP /api/v2/write (Line Protocol)
Note: MQTT broker is present but idle in the current ZHA deployment. Zigbee2MQTT is an alternative architecture that routes all data through MQTT (see Slide 10).
Notes: Let me trace the path that energy data takes from the physical meter all the way through to the database, because I think this is where the elegance of the system becomes clear.
It starts with the smart meter itself. Irish smart meters emit an infrared pulse for every watt-hour of electricity consumed. The Frient sensor clips over that optical port and counts those pulses, converting them into power in watts and cumulative energy in kilowatt-hours.
The Frient sensor sends those readings wirelessly over Zigbee to the Sonoff USB dongle plugged into the Pi.
The dongle passes the Zigbee radio frames to Home Assistant via a USB serial connection, where the ZHA integration — that stands for Zigbee Home Automation — decodes them and updates the entity states in the Home Assistant state machine. So at this point, Home Assistant knows the current power reading.
The InfluxDB integration inside Home Assistant then automatically writes every state change to the InfluxDB database over HTTP, using InfluxDB's line protocol format. This happens without any custom code — it's built into Home Assistant.
And that's it. From physical pulse to queryable time-series data, with no custom middleware, no bespoke code, just configuration.
I want to flag one thing for the technically curious: you'll see at the bottom that we have a note about MQTT. We do have a Mosquitto MQTT broker running in the stack, but in the current ZHA deployment, it's actually idle — Zigbee data doesn't pass through it. We have an alternative architecture using Zigbee2MQTT that routes everything through MQTT, which opens up more advanced use cases, and I'll cover that on slide ten.

## Slide 8
Key Services — What Each One Does
MTU SmartCORE HEMS
Interreg NWE SmartCORE
Home Assistant
• Central data hub & user dashboard
• Manages Zigbee devices via ZHA integration
• Syncs all sensor states → InfluxDB automatically
• Automation engine (backups, alerts)
• Trusted proxy via Nginx
InfluxDB 2
• Time-series database for all energy data
• Bucket: home_assistant | Org: hems
• Queried via Flux language / REST API
• Retains full history for research analysis
• UI accessible at /influx/ via Nginx
Nginx Reverse Proxy
• Single entry point — port 80 on host
• Basic auth (CONFIG_USER / CONFIG_PASSWORD)
• Routes / → HA, /influx/ → InfluxDB
• WebSocket upgrade headers for HA live UI
• Sub-filter rewrites InfluxDB JS asset paths
system-manager (Watchdog)
• Runs every 30 s on host network
• Restarts HA on new BalenaOS release
• Reboots device if internet down > 30 min
• Uses Balena Supervisor REST API
• iptables rules: Docker ↔ WiFi repeater
Mosquitto MQTT
• Message broker (port 1883)
• Ready for Zigbee2MQTT alternative arch
• Retained messages → sensor state on restart
• Persistence to mosquitto.db volume
• Currently idle (ZHA deployment)
led-status
• GPIO 17 → green LED (HA reachable?)
• GPIO 27 → blue LED (internet alive?)
• GPIO 22 → red LED (HA errors in log?)
• Pi 5 lgpio patch (chip=0)
• Polls every 2 seconds
Notes: Let me quickly walk through what each service actually does, because I want to give you a sense of how well-established and battle-tested each component is — we haven't had to write any of these from scratch.
Home Assistant is the largest open-source home automation project in the world, with over a million active installations. We use it as our data hub, Zigbee manager, and dashboard. It's the thing a householder would interact with.
InfluxDB is a purpose-built time-series database, widely used in industrial IoT and monitoring applications. Every sensor reading — timestamped to the second — goes in here and can be queried historically.
Nginx is a battle-hardened web server and reverse proxy. It's the gatekeeper — all web traffic comes in through it, it enforces basic authentication, and it routes requests to the right backend service.
The system-manager is the piece we wrote ourselves. It's a Python watchdog script that runs every thirty seconds. It checks whether a new software release has been pushed from Balena Cloud, and if so, gracefully restarts Home Assistant to pick up the changes. It also monitors internet connectivity and will reboot the Pi if the connection has been down for more than thirty minutes — because in a pilot home, we may not notice for days otherwise.
The led-status service is also ours. It drives three LEDs on the Pi's GPIO pins: green for Home Assistant healthy, blue for internet alive, and red if there are errors in the Home Assistant log. A green board is a happy board — even a non-technical householder can glance at it.
And Mosquitto is our MQTT message broker — lightweight, reliable, and the standard protocol for IoT messaging. It's ready and waiting for when we activate the Zigbee2MQTT path.

## Slide 9
Self-Healing & Remote Management
Zero-touch operation across distributed pilot deployments
MTU SmartCORE HEMS
Interreg NWE SmartCORE
BalenaOS — OTA Updates
Yocto-based container OS with Supervisor daemon
Push new Docker images from Balena Cloud → device auto-pulls
No SSH access required — fully managed via Balena dashboard
Balena App ID / Release ID tracked for graceful HA restart
system-manager Watchdog (30 s loop)
1. Stops wifi-repeater after 10 min (bandwidth management)
2. Detects new Balena release → graceful HA restart (2 min grace)
3. Pings google.com — reboots device if down > 30 min
4. Sets iptables rules on startup (Docker ↔ WiFi subnets)
LED Status Indicators (Physical Feedback)
🟢 GPIO 17 — Home Assistant reachable (internal ping)
🔵 GPIO 27 — Internet connectivity (8.8.8.8 ping)
🔴 GPIO 22 — Error state (scans HA log for ERROR keyword)
Allows non-technical householders to see system health at a glance
WiFi Onboarding — wifi-connect
On first boot (or lost WiFi): launches captive portal
Householder connects phone → selects home WiFi → enters password
NetworkManager configures WiFi via D-Bus on host
No LAN cable or technical knowledge required
Notes: One of the things I'm most proud of in this system is the self-healing capability, because it's what makes large-scale pilot deployment actually feasible.
Think about the logistics: twenty or thirty homes, spread across Munster, with a box running in each one. We cannot have a situation where one box gets a software bug and we have to drive out to the house to fix it. That's not sustainable.
BalenaOS solves the update problem completely. When we push a new Docker image to Balena Cloud, every device in the fleet automatically pulls the update and restarts the relevant container. Zero intervention required. We can fix a bug at eleven o'clock at night and have it deployed to all homes by midnight.
The system-manager watchdog handles the failure cases. If Home Assistant crashes or becomes unresponsive, the watchdog detects it and restarts it. If the internet goes down — which does happen in rural Irish homes — the watchdog waits thirty minutes and then reboots the entire Pi, which usually resolves connectivity issues caused by router or ISP problems.
The WiFi onboarding piece is important for the pilot deployment experience. When a box is first installed in a home, it has no WiFi credentials. What happens is: it broadcasts its own temporary WiFi network. The householder connects their phone to that network, gets a captive portal page — similar to what you'd see in a hotel — where they select their home WiFi and enter the password. The box connects, and that's the only time any technical setup is needed.
The physical LEDs are the last piece of the self-healing story. They give the householder a way to report back to us — "I can see the red light is on" — without needing to understand anything about the software.

## Slide 10
Extensibility & Future Work
The HEMS box is designed to grow with research requirements
MTU SmartCORE HEMS
Interreg NWE SmartCORE
Alternative: Zigbee2MQTT
Swap ZHA for Zigbee2MQTT container
All data routed through MQTT broker
Enables multi-subscriber architecture
→ Edge ML, alerting, custom exporters
MQTT Discovery → HA auto-creates entities
Mobile Access — Tailscale VPN
Add tailscale container (WireGuard VPN)
Researcher/admin accesses dashboard remotely
Peer-to-peer — no cloud server needed
Stable Tailscale IP survives dynamic WAN IP
TS_AUTH_KEY via Balena env var (never in repo)
Mobile Access — Cloudflare Tunnel
Add cloudflared container
4 outbound HTTPS connections to Cloudflare
Public HTTPS URL: hems.yourdomain.com
No port forwarding or router changes
Cloudflare Access for pre-auth layer (free)
Additional Sensors
Any Zigbee sensor pairs via ZHA/Z2M
Temperature, humidity, occupancy, gas
EV charger monitoring (eesmart-d2l path)
Clamp-on CT sensors via ESPHome/WiFi
Solar PV integration (planned)
Data Export & Integration
InfluxDB REST API → SmartCORE EU platform
Export to CSV / Parquet for research
Grafana compatible (Flux queries)
MQTT → Node-RED for custom pipelines
REST hook → external ML inference
Known Gaps to Resolve
eesmart-d2l: TCP proxy in Nginx but no container
No TLS on Nginx (plain HTTP on LAN only)
MQTT allow_anonymous (harden for production)
template_sensors/ not in git (on-device only)
Pilot home deployment tooling — in progress
Notes: Now I want to talk about where the system goes from here, because one of the key design decisions was to make this extensible without needing hardware changes.
The first extension I want to highlight is the Zigbee2MQTT alternative architecture. Currently, Zigbee data goes directly into Home Assistant via the ZHA integration. An alternative — which we've designed and documented but not yet activated — is to run a Zigbee2MQTT container instead. This routes all Zigbee data through the MQTT broker first. Why does that matter? Because with MQTT, multiple services can subscribe to the same data stream simultaneously. So you could have Home Assistant, a custom analytics service, and a cloud uploader all receiving the same sensor readings in parallel, without any of them interfering with the others.
For mobile access — so researchers or householders can check their energy data from outside the home — we have two options designed and ready to implement. The first is Tailscale, which creates a peer-to-peer VPN tunnel to the Pi. The second is Cloudflare Tunnel, which gives the box a public HTTPS URL without needing to open any ports on the home router. Both are activated by adding a single container and an API key — no code changes to the existing stack.
And finally, for data export to the SmartCORE EU platform, the InfluxDB REST API is the natural integration point.

## Slide 11
MTU's Research Contribution
What we bring to SmartCORE NWE
MTU SmartCORE HEMS
Interreg NWE SmartCORE
What MTU Has Built
• Full open-source HEMS software stack
  – Containerised, reproducible, version-controlled
  – Deployable from a single docker-compose.yml
• Raspberry Pi 5 validated deployment
  – Pi 5 GPIO lgpio patch for led-status
  – aarch64/arm64 Docker image selection
• Self-healing watchdog architecture
  – Balena Supervisor API integration
  – Graceful HA restart on new firmware
• Technical documentation & architecture reference
  – ARCHITECTURE.md, COMPONENTS.md
  – MQTT & Mobile Access reference
  – PlantUML system diagrams
Impact for SmartCORE Partners
Any partner can clone repo & deploy
No proprietary hardware lock-in
OTA updates mean pilot homes update silently
Full data access — no vendor API restrictions
Adapts to local smart meter standards
Research Outputs (Planned)
Peer-reviewed publication on HEMS architecture
Open dataset from pilot homes (anonymised)
Comparison: ZHA vs Zigbee2MQTT performance
Energy baseline per household profile
Integration template for EU SmartCORE platform
Technology Readiness
TRL 4 → 5 transition (lab → pilot validated)
Core stack functional on Pi 5 hardware
Sensor integration confirmed end-to-end
Pilot deployment tooling in progress
Notes: I want to be clear about what MTU has specifically contributed to this project, because I think it's significant.
We've built a complete, open-source, production-ready HEMS software stack from the ground up. Everything is containerised, reproducible, and version-controlled. Any engineer can clone the repository, run a single command, and have the entire system running — either on a Pi or on their own laptop for development.
We've validated this on Raspberry Pi 5 hardware specifically — and that's non-trivial, because the Pi 5 has architectural differences from previous Pi versions that required patches. In particular, the GPIO subsystem uses a different chip number, which broke the LED status software until we identified and fixed it.
We've written detailed technical documentation: a full architecture reference, a per-component guide, and a technical reference for the MQTT and mobile access architecture. This means that if any partner wants to understand the system, or if a new team member joins the project, the documentation is there.
In terms of research outputs, we're planning a peer-reviewed publication on the architecture, an anonymised dataset from the pilot homes, and a comparison study between the ZHA and Zigbee2MQTT approaches.
In terms of technology readiness — we're transitioning from TRL 4, which is lab validation, to TRL 5, which is pilot-validated. The core stack is functional and confirmed end-to-end on real hardware. Pilot deployment tooling is the next step.

## Slide 12
Current Status & Roadmap
Early prototype → pilot deployment
MTU SmartCORE HEMS
Interreg NWE SmartCORE
✓ Stack Running
All 8 containers operational on Pi 5
✓ Sensor Data
Frient → InfluxDB end-to-end confirmed
✓ OTA Updates
BalenaOS push validated in lab
✓ Self-Healing
Watchdog tested (reboot, HA restart)
~ Mobile Access
Architecture designed, implementation pending
→ Pilot Homes
Deploy to 5-10 homes
Notes: Let me bring you up to date on where we are right now and what the next twelve months look like.
Looking at the six status indicators across the top: the stack is running — all eight containers are operational on Pi 5 hardware. Sensor data is flowing end-to-end from the Frient sensor through to InfluxDB, confirmed in the lab. Over-the-air updates via BalenaOS have been validated. And the self-healing watchdog has been tested for both the HA restart and the device reboot scenarios.
Mobile access is in an intermediate state — the architecture is fully designed and documented, and the implementation is straightforward, but it's not yet activated. And pilot home deployment is where our focus is now — we're in the site survey phase and targeting first installations in Q3 of this year.
On the roadmap: Q2 2026 is about pilot preparation — finalising the deployment tooling, activating mobile access, and hardening the MQTT security before we put boxes into homes. Q3 is the first wave of pilot deployments, targeting five to ten homes with live data flowing to the SmartCORE platform. Q4 is about scaling to twenty homes and starting the energy baseline analysis. And by 2027 we're looking at full dataset analysis, a second-generation HEMS design based on what we learn, and sharing results across all NWE partner countries.
The short version: the system works, we're ready to deploy, and the focus now is execution.

## Slide 13
Thank You
Questions & Discussion
Notes: And that brings me to the end of the presentation.
To summarise in three sentences: MTU has built an open-source, self-healing, containerised energy monitoring gateway on Raspberry Pi 5 hardware. It captures real-time energy data from smart meters via Zigbee sensors and stores it in a local time-series database. It's designed to be deployed in pilot homes with zero on-site maintenance and full remote manageability.
The system is working in the lab, and we're ready to start deploying.
I'm very happy to take questions now — whether on the technical architecture, the deployment approach, or how this integrates with what other partners are building. And if any of you want to go deeper on any aspect — particularly if you're thinking about replicating something similar in your own country — please do come and find me afterwards.
Thank you.